LPWAN

Low power wide area networks (LPWAN) technologies focus on long-distance communication applications with energy constraints, which usually comes at the cost of a reduced bit rate.

To ensure reliability, efficient signal demodulation techniques are paramount to enable long-distance communications and better service quality. Thus, reducing the need for signal retransmission, which entails congesting thescarce spectrum resources. Spectrum efficiency is particularly important in the unlicensed industrial, scientific, and medical (ISM) spectrum band since this band is available to the public and requires minimal fees to access

Lora
A prominent LPWAN modulation technique is LoRa, providing a suitable platform for many IoT applications.

LoRa can be operated on the license free sub-gigahertz bands, for example, 915 MHz, 868 MHz, and 433 MHz. It also can be operated on 2.4 GHz to achieve higher data rates compared to sub-gigahertz bands, at the cost of range. These frequencies fall into ISM bands that are reserved internationally for industrial, scientific, and medical purposes.

Ultra low power - LoRaWAN end devices are optimized to operate in low power mode and can last up to 10 years on a single coin cell battery.
- Long range - LoRaWAN gateways can transmit and receive signals over a distance of over 10 kilometers in rural areas and up to 3 kilometers in dense urban areas.
- Deep indoor penetration - LoRaWAN networks can provide deep indoor coverage, and easily cover multi floor buildings.
- License free spectrum - You don’t have to pay expensive frequency spectrum license fees to deploy a LoRaWAN network.
- Geolocation- A LoRaWAN network can determine the location of end devices using triangulation without the need for GPS. A LoRa end device can be located if at least three gateways pick up its signal.
- High capacity - LoRaWAN Network Servers handle millions of messages from thousands of gateways.
- Public and private deployments - It is easy to deploy public and private LoRaWAN networks using the same hardware (gateways, end devices, antennas) and software (UDP packet forwarders, Basic Station software, LoRaWAN stacks for end devices).
- End-to-end security- LoRaWAN ensures secure communication between the end device and the application server using AES-128 encryption.
- Firmware updates over the air - You can remotely update firmware (applications and the LoRaWAN stack) for a single end device or group of end devices.
- Roaming- LoRaWAN end devices can perform seamless handovers from one network to another.
- Low cost - Minimal infrastructure, low-cost end nodes and open source software.
- Certification program- The LoRa Alliance certification program certifies end devices and provides end-users with confidence that the devices are reliable and compliant with the LoRaWAN specification.
- Ecosystem- LoRaWAN has a very large ecosystem of device makers, gateway makers, antenna makers, network service providers, and application developers.
Lora Kullanım alanları:

COVID-19 Support
Smart Agriculture
Smart Buildings
Smart Cities
Smart Electricity Metering
Smart Environment
Smart Gas Metering
Smart Healthcare
Smart Home
Smart Homes & Buildings
Smart Industrial Control
Smart Metering
Smart Retail
Smart Supply Chain & Logistics
Smart Water Metering

# A Google map showing the location of the three LoRa Gateways installation in Glasgow city centre. Markers map the locations from where the end-device received LoRaWAN RSS indicators.

City of Calgary LoRaWAN signal coverage map

Measuring soil condition for urban canopy maintenance and water valve status remotely, which saves time, conserves resources and provides more accurate and timely data.
- City-wide air quality sensors enable us to monitor the environment.
- River sensors provide ongoing updates on flood concerns, allowing us to better plan and prepare for any high-water events.

### LoRaWAN
LoRaWAN is a Media Access Control (MAC) layer protocol built on top of LoRa modulation. It is a software layer which defines how devices use the LoRa hardware, for example when they transmit, and the format of messages.

# Istanbul Airport, Biggest Industrial IoT Network in Airport Business
Istanbul Airport has an area of 76.5 million square meters

Skysens is the official wireless industrial IoT network provider for Istanbul Airport and is currently operating this large network.
Teams in Istanbul Airport are instantly monitoring many different infrastructures on a single network including waste pumps, water and electric meters, doors, ILS systems, UPS systems and other critical assets. There are more than 3000 points in the airport and this is expected to be 10000 by the end of the project. All the data is currently gathered from the Skysens end-modules, monitored and analyzed with the Skysens IoT platform.
Skysens’s plug-and-play end modules provide a wide range of application areas and can be used in many different infrastructures for diverse purposes. Energy and water consumption, temperature and humidity of the environment or specific machines, different assets’ current conditions or maintenance needs, electrical leakages, location tracking for the employees or vehicles or unauthorized door openings can be monitored in minutes through the same network, without the need of any infrastructural costs.

Döküman linkleri

https://www.thethingsnetwork.org/docs/lorawan/what-is-lorawan/

https://www.semtech.com/lora/what-is-lora

- https://www.semtech.com/lora/lora-applications
- https://www.semtech.com/lora/why-lora
- https://lora-developers.semtech.com/documentation/technical-documents
- https://lora-alliance.org/wp-content/uploads/2020/11/lorawan-regional-parameters-v1.1ra.pdf
https://www.researchgate.net/publication/351449349_LoRa_Signal_Demodulation_Using_Deep_Learning_a_Time-Domain_Approach?enrichId=rgreq-94e7f428ec8f15fa5157516a161c0694-XXX&enrichSource=Y292ZXJQYWdlOzM1MTQ0OTM0OTtBUzoxMDIxNzYwMzk2ODYxNDQxQDE2MjA2MTgwNzA5MTc%3D&el=1_x_3&_esc=publicationCoverPdf